## Slide 1: Assignment 3 HARP Emulator
TA: Si Li
ECE 8823
Fall 2015

## Slide 2: HARP ISA - C. Kersey
Full predication - each instruction can be predicated
SIMT
Little endianness
RISC-like
Byte addressable
Configurable Architecture
Assignment Architecture: 4w/8/8/8/8
  4 byte registers and addresses (32 bit words)
  word-based instruction encoding (32 bits)
  8 general purpose registers (GPRs)
  8 predicate registers
  8 SIMD lanes
  8 warps (thread groups)

## Slide 3: Instruction Encoding
[P][PReg][Opcode][Operand][Predicate operand]... [Immediate]
P - 1 bit predicate enable bit: set to 1 if PReg is valid
  if P=0, instruction always executes
PReg - Predicate register, log2(#pregs) 8 PRegs = 3 bits
Opcode - 6 bits
Operand - log2(#GPRs) - 8 registers = 3 bits
Predicate Operands - log2(#pregs) (optional)
Immediate - all remaining bits
Example: add %dest, %src1, %src2 [P][PReg][Opcode][Operand][Operand][Operand]

## Slide 4: Instructions
Nop nop
Load/store ld %dest, %base, #Offset
Predicate instructions andp @dest, @src1, @src2
Value tests rtop @dest, %src
Arithmetic/logic addi %dest, %src1, #IMM
Floating point arithmetic mul %dest, %src1, %src2
Control flow jalr %link, %reg

## Slide 5: Example Program Fragment
sort subroutine load %r4 from stack load %r5 from stack %r2 = %r4 - %r5 @p0 = (%r2 == 0) ? 0 : 1 jump to _sort_8 if p0 == 0
_sort_4: ld %r0, %sp, #16 ld %r4, %r0, #0 ld %r0, %sp, #12 ld %r5, %r0, #0 sub %r2, %r4, %r5 rtop @p0, %r2 @p0 ? jmpi _sort_8

## Slide 6: Emulator Overview
Read in binary as a vector of bytes
Initialize register file
Load the first word as an instruction (PC=0)
Parse instruction - determine opcode, operands
Execute instruction
Execute load/store operation
Update register file
Update PC

## Slide 7: Instruction Execution
1 Load instruction at PC address
2 Read from register file
3 Execute instruction
4.1 Load/store
4.2 Write back to register file
4.3 Update PC
Load Instruction
Execute
Load/Store
Memory
Register File
PC
1
1
2
3
4.2
4.3
4.1

## Slide 8: Device Output
Output device at x800..00
One character (1 byte) per store/instruction/lane
Write output as a stream of bytes from one thread
Example: if (addr == 0x80000000 && threadID == 0) putc(data, outputFile);

## Slide 9: Questions?